## Slide 1
INFRARED ATMOSPHERIC SOUNDING INTERFEROMETER
OF NEW GENERATION PROGRAM:
GENERAL STATUS OVERVIEW
F.BERMUDO . IASI-NG PROJECT MANAGER for IASI-NG TEAM
CENTRE NATIONAL D’ÉTUDES SPATIALES (TOULOUSE, FRANCE)
IASI 2021 CONFÉRENCE
EVIAN, FRANCE . 06 – 10 DECEMBER 2021

## Slide 2
IASI-NG CNES PROGRAM PART OF EUMETSAT POLAR SYSTEM SECOND GENERATION PROGRAM (EPS-SG)
EMBARKED ON
METOP SG-A SATELLITES SERIES DEVELOPED BY ESA
• Operational observations from polar orbit
• 2024 to 2044 timeframe
• 3 successive flight models

## Slide 3
CLIMATE
MONITORING
ATMOSPHERIC CHEMISTRY
NUMERICAL
WEATHER
PREDICTION

## Slide 4
IASI-NG
PROJECT
3 instruments to be flown on the series Metop-SG A Satellites
Level 1 Operational Processor (L1CPOP) processing scientific data up to level 1C (Atmospheric Spectra)
Technical Expertise Center (IASTEC) performances monitoring in orbit

## Slide 5
IASI-NG
PERFORMANCES
Continuity of IASI’s first generation operational observations
SPECTRAL RESOLUTION
SPECTRAL SAMPLING
RADIOMETRIC
NOISE
SOUNDING PIXEL SIZE DIAMETER
RADIOMETRIC
CALIBRATION
0.25 CM-1
(2 times better than IASI)
~17000 Spectral Channels
(2 times better than IASI)
NedT ~ 0.1K
(2 times better than IASI)
NedT ~ 0.25K
(2 times better than IASI)
12 Km
SPECTRAL RESOLUTION
SPECTRAL SAMPLING
0.25 CM-1
(2 times better than IASI)
~17000 Spectral Channels
(2 times better than IASI)
RADIOMETRIC
NOISE
RADIOMETRIC
CALIBRATION
NedT ~ 0.1K
(2 times better than IASI)
NedT ~ 0.25K
(2 times better than IASI)
Improvement of some essential performances measurement
Allowed via a wider field of analysis

## Slide 6
IASI-NG
INSTRUMENT CONCEPT
Interferometer: 2 beams with different optical paths (beam splitter and moving mirrors )
Different optical paths : creation of Interferogram’s by beam recombination
Interferogram’s : breakdown and spectral analysis

## Slide 7
IASI-NG
INTRUMENT CONCEPT
Off the axis: field effects appear (rings of parasitic interference) affecting measurement quality
Compensating for the field effects is essential

## Slide 8
IASI-NG
INSTRUMENT CONCEPT
Field effects compensation: inserting dynamically glass of varying thickness
Synchronization between optical path difference and variation in glass thickness
Achieved through 2 pairs of prisms, synchronized via an unique device movement

## Slide 9
IASI-NG
INSTRUMENT CONCEPT
Performances improvement allowed by innovative instrumental concept proposed by Airbus Defense and Space
First implementation in space of a Mertz Interferometer

## Slide 10
IASI-NG
DEVELOPMENT STATUS:
MAIN MILESTONES ACHIEVED
Consolidation of instrument definition with completion of Instrument Critical Design review (Early 2020)
Completion of Engineering model test campaign in 2021
Proto Flight Model integration started

## Slide 11
IASI-NG
DEVELOPMENT STATUS:
MAIN MILESTONES ACHIEVED
Consolidation of System definition with completion of On-ground algorithm processing:
To correct the imperfection of the instrument : calibration of the data, spectrally and radiometrically
Equalization of the provided spectra with an unique Spectral Response Function, for all channels and all pixels
Geo-localize the sounder pixels and information about the scene description inside the pixel Field Of View (radiance classification)

## Slide 12
IASI-NG
DEVELOPMENT STATUS:
MAIN MILESTONES ACHIEVED
Consolidation of System definition with completion of On-ground algorithm processing:
Calibration of the data, spectrally and radiometrically
Equalization of the provided spectra with an unique Spectral Response Function, for all channels and all pixels
First Mission performances assessment achieved with success of System Critical Design review (Mid 2020)

## Slide 13
IASI-NG
DEVELOPMENT STATUS:
MAIN MILESTONES ACHIEVED
Consolidation of System definition with IASTEC requirements and functional breakdown:
ROOTS functions
  Instrument and L1C processing monitoring (quality flags , parameter trend)
  Generation of new OB/OG SW updates parameters
  Visualization tool
  Routine processing chains
GENIE functions : expertise function tool for fine performances estimation and investigation

## Slide 14
IASI-NG
DEVELOPMENT STATUS:
MAIN MILESTONES COMING SOON
Completion of Proto Flight Model integration :
COMPLETED !!!
CBB
CBB FPI
CBB CAG
WBB
WBB
Exhaustive Qualification and test campaign with performances test under Vacuum early 2022

## Slide 15
IASI-NG
DEVELOPMENT STATUS:
MAIN MILESTONES COMING SOON
Completion of Proto Flight Model integration and test campaign with performances test under Vacuum early 2022
Sun acquisition with comparison with Compact High-Spectral-Resolution Infrared Spectrometer (CHRIS) acquisition

## Slide 16
IASI-NG
DEVELOPMENT STATUS:
MAIN MILESTONES COMING SOON
Completion of Proto Flight Model integration and test campaign with performances test under Vacuum early 2022
Integration and test campaign of IASI-NG instrument on Metop SG A satellite in 2022-2023

## Slide 17
IASI-NG
DEVELOPMENT STATUS:
MAIN MILESTONES COMING SOON
Completion of Proto Flight Model integration and test campaign with performances test under Vacuum early 2022
Integration and test campaign of IASI-NG instrument on Metop SG A satellite in 2022-2023
Performances checked during Satellite Thermal Vacuum in 2022

## Slide 18
IASI-NG
DEVELOPMENT STATUS:
MAIN MILESTONES COMING SOON
Integration and test of the Version 1 (Partial Processing) Level 1C processor in the EUMETSAT Payload Processing Center in 2022
Integration and test of the Version 2 (Full processing) of the Level 1C processor in the EUMETSAT Payload Processing Center in 2023
Completion of development and Operational Qualification of Technical Expertise Center in 2023

## Slide 19
IASI-NG
DEVELOPMENT STATUS:
MAIN MILESTONES COMING SOON
Integration and test of the Level 1C processor in the EUMETSAT Payload Data Acquisition and Processing center and Operational qualification of Technical Expertise Center in 2023
Launch campaign and launch from Guyana Space Center in 2024
In Orbit Verification phase (3 months ) and Cal/Val phase ( 6 months)

## Slide 21
THANK YOU FOR YOUR ATTENTION !